| LH149QMG发动机主要技术规格 Main technical specifications of LH149QMG engine |
| --- |
| 型号 Model | LH149QMG |
| 型式 Type | 单缸、四冲程、点燃 Single cylinder, four-stroke, ignited |
| 标定功率及标定转速(曲轴输出）kW/r/min Rated power and rated speed (kW/r/min) | 4.9/7500〜8000 |
| 标定功率及标定转速(输出轴输出）kW/r/min Rated power and rated speed (output shaft) kW/r/min | 3.43/7500〜8000 |
| 标定功率允许在配套整车上测定后轮功率kW/km/h Rated power, rear wheel power allowed to be measured on the supporting complete vehicle (kW/km/h) | 3.1/70〜Vmax |
| 最大功率及转速(曲轴输出)kW/r/min Max. power and rated speed (crankshaft output) (kW/r/min) | 5.8/7500〜8000 |
| 最大扭矩及相应转速（曲轴输出）N.m/r/min Max. torque and corresponding speed (crankshaft output) (N·m/r/min) | 6.4/5500〜6500 |
| 最低燃油消耗率g/kW. h (或配套整车上测定经济油耗l/100km) Min. fuel consumption rate g/kW.h (or fuel mileage measured on supporting complete vehicle l/100km) | 403(2.5) |
| 最低空载稳定转速（怠速）r/min Min. no-load steady speed (idle) r/min | 1600土100 |
| 气缸直径mm Cylinder diameter (mm) | 49.0 |
| 活塞行程mm Piston stroke (mm) | 54 |
| 总排量ml Total displacement (ml) | 101.8 |
| 压缩比 Compression ratio | 9.5:1 |
| 曲轴连杆比 Connecting rod ratio of crankshaft | 0. 3075 |
| 发动机布置形式 Engine arrangement form | 卧式 Horizontal |
| 点火提前角 Ignition advance angle | 5° （2400rpm) |
| 进气方式 Air intake type | S0HC |
| 汽油牌号 Gasoline grade | 90 |
| 润滑油牌号 Lubricant grade | 15W/40 |
| 外形尺寸（aXbXh) mm Size (axbxh) mm | 640X410X365 |
| 净质量kg Net weight (kg) | 25.5 |