| 整车 Full vehicle | 型号 Model | LH400ATV-2D |
| --- | --- | --- |
|  | 长 X 宽 X 高 Length X Width X Height | 2170×1145×1225 |
|  | 轮距 Wheel track | 1285mm |
|  | 座高 Seat height | 915mm |
|  | 最小离地距离 Min. ground clearance | 253mm |
|  | 最小转弯直径 Min. turning diameter | 3277mm |
|  | 油箱容量 Fuel tank capacity | 14.5L |
|  | 重量 Weight | 320kg |
|  | 载重量 Dead weight capacity | 150kg |
|  | 驱动 Drive | 2 驱/4 驱切换 2-wheel drive/4-wheel drive switching |
| 动力性能 Dynamic performance | 型号 Model | LH180MQ |
| 安全操控 Safety manipulation | 制动形式 Brake type | 液压盘式制动 Hydraulic disc brake |
|  | 悬挂方式 Suspension type | 前轮: 麦弗逊独立悬挂； Front wheel: McPherson independent suspension; 后 轮: 双 A 臂独立悬挂 Rear wheel: double A-arm independent suspension |
|  | 减震器类型 Shock absorber type | 螺旋弹簧油阻尼式 Spiral spring with oil damping |
|  | 轮辋规格及形式 Rim specifications and forms | 前轮辋: AT25X8-12 Front wheel rim: AT25X8-12 后轮辋: AT24X10-12 Rear wheel rim: AT24X10-12 |
|  | 胎规格及气压 Specification and air pressure of tire | Front:35kPa;Rear: 35kPa |
| 证书 Certificate | EEC |
| 可选颜色 Available colors | 红色，白色，蓝色，军绿，黑色，迷彩 Red, white, blue, army green, black, camouflage |
| 40 尺高柜集装箱数量 Number of 40-foot high cabinet containers | 27 |